Comparison of CORSIKA hadronic interaction generators with GRAPES-3 data
Departmental Project 2
Presented by – Mohit Saharan
Advisor – Dr. Pravata K. Mohanty

---
Outline
Cosmic rays
Motivation
Simulation of monoenergetic showers
Simulation of showers with variable energy
Comparison of simulation results with GRAPES-3 data

---
Cosmic rays
- High energy particles originating from outer space
- Mostly protons (90%), helium (9%), heavier nuclei,
  minute fraction of high energy electrons, positrons
- Observable shower secondaries
  - Electron, muon, hadron, and photons
  - Characteristics depend on energy and mass of the primary cosmic ray particle
- Source and propagation?
- Composition of cosmic rays
- Simulation of air showers
  - Not reliable

---
Motivation
- To find the best suited hadronic interaction generator for GRAPES-3 experiment
- Cosmic ray composition
  HOW?
- Simulation of monoenergetic air showers using different hadronic interaction generators (Mumbai)
  - varying primary energy
  - varying primary mass
- Realistic simulation of showers (Ooty)
- Comparison of the resulting muon multiplicity (number of muons per shower) distributions

---
GRAPES-3 Experiment
- Located in Ooty, India; 2200 m above
  m.s.l.
- 400 plastic scintillator detectors (1 m2 each)
- Array covers an area of 25000 m2
- Large area (560 m2) tracking muon detector
- Muon detector
  - 16 muon modules (35 m2 each)
  - Each module has 232 proportional counters

---
CORSIKA simulation package
- High energy hadronic interaction generators
  - SIBYLL
  - QGSJETII
- Low energy hadronic interactions were treated using FLUKA

---
Simulation of monoenergetic showers: Part 1
- Primary
  - H
- θ = 0°
- E = 10 TeV, 100 TeV, and 1000 TeV
- 50,000 events - 10 TeV and 100 TeV
- 2400 events -1000 TeV
- Pre-LHC: SIBYLL-2.1 and QGSJETII-03
- Post-LHC: SIBYLL-2.3c and QGSJETII-04

---
Muon multiplicity distributions
SIBYLL
10 TeV
100 TeV
1000 TeV
Muon Multiplicity
QGSJETII
10 TeV
1000 TeV
100 TeV
No. of events

---
Pre-LHC and Post-LHC generators
SIBYLL
QGSJETII
- More muons by Post-LHC:
  - SIBYLL: 12% to 19 % more
  - QGSJETII: 6% to 15% more

---
Pre-LHC and Post-LHC generators
SIBYLL
QGSJETII
- More muons by QGSJETII:
  - Pre-LHC: 6% to 9% more
  - Post-LHC: 2% to 3% more

---
Simulation of monoenergetic showers:
Part 2
- θ = 0°
- E = 10 TeV, 100 TeV, and 1000 TeV
- 50,000 events at 10 TeV and 100 TeV
- 2400 events at 1000 TeV
- At 1000 TeV, data generated only for H, N, and Fe
- Comparison of post-LHC generators
- PCRs
  - Lighter (H, He)
  - Medium (C,N,O)
  - Heavier (Al, Fe, Co)

---
Muon multiplicity distributions
SIBYLL
10 TeV
Muon Multiplicity
QGSJETII
100 TeV
1000 TeV
10 TeV
100 TeV
1000 TeV
No. of events

---
Simulation for E = 10 TeV
- Muon multiplicity increases with mass number
- More muons by Fe w.r.t H:
  - SIBYLL: 77% more
  - QGSJETII: 85% more
- QGSJETII vs SIBYLL
  - 3% to 7% more
  - Difference increases with mass number

---
Simulation for E = 100 TeV
- Muon multiplicity increases with mass number
- More muons by Fe w.r.t H:
  - SIBYLL: 56% more
  - QGSJETII: 61% more
- QGSJETII vs SIBYLL
  - 2% to 5% more
  - Difference increases with mass number

---
Simulation for E = 1000 TeV
- Muon multiplicity increases with mass number
- More muons by Fe w.r.t H:
  - SIBYLL: 48% more
  - QGSJETII: 49% more
- QGSJETII vs SIBYLL
  - 2% to 3% more
  - Difference is relatively less

---
Simulation of showers with variable energy
- Simulation of monoenergetic showers
  - Improvement in Post-LHC generators
  - Characteristics of generators: 1) for different primaries, 2) at different energies
  - Can’t do realistic simulations directly

---
Proton initiated showers
Bin No	Energy Range (TeV)	No. of events
		Pre-LHC (SIBYLL)
1	63.10 – 100.00	99,900
2	100.00 – 158.49	45,700
3	158.49 – 251.19	20,900
4	251.19 – 398.11	9,500
5	398.11 – 630.96	4,400
6	630.96 – 1000.0	2,000

---
Proton initiated showers
Bin No	Energy Range (TeV)	No. of events
		Pre-LHC (SIBYLL)	Post-LHC (SIBYLL)
1	63.10 – 100.00	99,900	30,00,000
2	100.00 – 158.49	45,700	13,72,000
3	158.49 – 251.19	20,900	6,27,000
4	251.19 – 398.11	9,500	2,86,500
5	398.11 – 630.96	4,400	1,31,100
6	630.96 – 1000.0	2,000	59,800
- ~30 times larger data set; generated in Ooty cluster (~1200 cores)
- Analysis framework improved
  - Realistic muon detection for simulation data
- Testing

---
Proton initiated showers
Bin No	Energy Range (TeV)	No. of events
		Pre-LHC (SIBYLL)	Post-LHC (SIBYLL)
1	63.10 – 100.00	99,900	30,00,000
2	100.00 – 158.49	45,700	13,72,000
3	158.49 – 251.19	20,900	6,27,000
4	251.19 – 398.11	9,500	2,86,500
5	398.11 – 630.96	4,400	1,31,100
6	630.96 – 1000.0	2,000	59,800
- 0°<θ<25°
- Shower size (Ne) - 104.0 to 105.5 with bin width = 100.5
- Comparison with 2014 data

---
Comparison of simulation results with GRAPES-3 data
Shower Size – 104.0 to 104.5
Shower Size – 104.5 to 105.0
Work on GRAPES-3 data – Diptiranjan Pattanaik

---
Summary
- Post-LHC generators give higher muon multiplicity
  - SIBYLL: 12% - 19% more muons in Post-LHC
  - QGSJETII: 6% - 15% more muons in Post-LHC
- In Post-LHC, QGSJETII gives higher muon multiplicity than SIBYLL
  - 2% to 7% more muons in QGSJETII
  - Difference decreases with increasing energy
- Proton initiated shower data
  - Post-LHC simulation data shows better agreement with GRAPES-3 data

---
Future plans of GRAPES-3 group
- Generation of variable energy showers with He, N, Al, and Fe
- Comparison with GRAPES-3 data to find the composition of cosmic rays for 63 TeV<E<1000 TeV
  - To find out the generator which agrees with GRAPES-3 data

---
It’s a team effort!
GRAPES-3 Group
Meeran Zuberi
Jhansi Bhavani
Diptiranjan Pattanaik
Fahim Varsi
Medha Chakraborty
Shekhar Sharma
Piyush Kumar
Prof. Sunil Gupta
Prof. S. Dugad
Dr. P. K. Mohanty
Mr. B Hari Haran
Mr. S. D. Morris
Mr. L. V. Reddy
Mr. P. K. Naik
Team at Ooty and other collaborators